## Slide 1: Job Hazard Analysis (JHA)
Notes: 1

## Slide 2: Job Hazard Analysis (JHA)
What is it?
Why do I have to do it?

## Slide 3: JHA (or JSA) Defined
A Job Hazard Analysis is a technique that focuses on job tasks as a way to identify hazards before they result in injury, illness, property damage, or worse
It focuses on the relationship between the worker, the task, the tools, and the work environment
After identifying uncontrolled hazards, steps are taken to eliminate or reduce them to an acceptable risk level
Reference: OSHA 3071 Guidebook

## Slide 4: Workplace injuries
Majority of disabling workplace injuries happen to workers who are in their first year with a new employer
Little or no safety training
Unsafe work procedures
Inadequate Personal Protective Equipment (PPE)
No safety oversight

## Slide 5: Why do we all have to do this?
Each lab and each project has unique hazards
One-time training is insufficient: better to drill important concepts
Human beings are unreliable operators, and training is the least reliable way of preventing injuries unless it is thorough

## Slide 6: Steps to follow:
Assemble group of people knowledgeable in tasks involved in a lab or research project
Break down jobs involved in a lab or project into steps, and identify potential hazards in each step
Identify “controls” for each hazard
Train all involved personnel and students
Document the hazards, safe procedures, and training sessions in writing

## Slide 7: People who will do JHA
Course Coordinator and Lab Coordinator for teaching labs. Input from instructors, TA’s, students.
Team advisor and student captains for team projects.
Principle Investigator(s) for research projects. Input from student researchers.
All of the above should use expertise of COE techs and safety personnel as needed.

## Slide 8: Breaking down the job
Not too many steps, not too few steps
Get out of your normal mode of thinking and imagine things that can go wrong
Of the things that can go wrong, prioritize the ones that are:
    Most Likely
    Most dangerous

## Slide 9: A few common hazards
Chemical (toxic, flammable, corrosive, explosive)
Unexpected release of stored mechanical energy (springs, compressed gasses, dropped weights)
Electrical hazards (shock/electrocution, fire, electrostatic discharge)
Mechanical (blades, crushing, rotating machinery, abrasion)
Radiation (lasers, radioactive materials)
Biohazard (toxins, infectious agents, carcinogens)
Ergonomic (lifting heavy weights, repetitive motion, eye strain)

## Slide 10: Training
Train instructors and TA’s thoroughly
Train students before they do anything in the lab
Consider giving students a safety test as part of the grade for teaching labs, and as a qualifying litmus test for participation in a project

## Slide 11: Controls
From most effective to least effective:
Remove the danger altogether if not critical to class/project
Guard the danger
Provide personal protective equipment
Provide instructions, training, warnings

## Slide 12: Documentation
Document hazards and safe operating procedures on standard form
Keep this list on file
Provide this list to all students/instructors involved with lab or project before they start work
Keep a signup sheet with names, dates, and signatures, verifying that training occurred

## Slide 13: Examples
ME 220L Safety Form
Ethanol Distillation Safety Form
Blank Safety Form: Learn by doing!